## Slide 1: LUMPS and BUMPS
Dr. Rose Lee

## Slide 2: Clinical History
First symptom: how did they first notice lump
Duration: how long has it been present
Progression: has it increased/decreased in size or remained stable since then, does it go away
Multiplicity: previous/other lumps
Associated symptoms: fever, redness, pain, weight change, associated with menstrual cycle
Past history: trauma, surgery, prior malignancy

## Slide 3: Clinical Findings
Is palpable or visible to you?
Is it mobile or fixed?
Is it hard or soft?
Look for redness or swelling
Is there drainage or a sinus tract?

## Slide 4: Role of Ultrasound
Confirm presence of a mass
Location of mass
Characterize mass
  Cyst vs solid
  Vascularity
  Dynamic information – compression
However, majority of soft tissue masses have nonspecific appearance: DDx driven by location

## Slide 5: Scanning Protocol
Use a high frequency linear transducer first
May need to change to lower frequency probe if patient is large or mass extends into deep soft tissues or curvilinear
If the mass is small, trap mass between two fingers to hold down while scanning
Start scanning the nearby, NORMAL, uninvolved area to appreciate normal anatomy (can scan contralateral side too)

## Slide 6: Scanning Protocol
First image mass to show relationship with respect to soft tissue layer
  Large FOV
  Scan along the border of the mass
Then image to show mass close up in detail to assess edges, internal characteristics, and vascularity (may need standoff pad or lots of gel)
Take at least 3-5 images in sagittal and axial through the mass or more if large

## Slide 9: Location Location Location
Body location:
  Draw an image
  Describe with respect to external landmarks
Soft tissue layer:
  Dermal: thin hyperechoic layer
  Subcutaneous: hypoechoic fat interspersed with hyperechoic linear (connective tissue septa)
  Fascial: thin hyperechoic layer
  Muscle: hypoechoic cylindrical structures, with hyperechoic connective tissue, surrounding them
  Bone: strong hyperechoic shadow

## Slide 10: Normal Soft Tissues

## Slide 11: Muscle layer longitudinal
Notes: Muscles longitudinal

## Slide 12: Muscle layer transverse
Notes: Muscles transverse

## Slide 13: Normal Soft Tissues – axilla

## Slide 14: Normal Soft Tissues-chest wall
Notes: Chest wall

## Slide 15: Normal Soft Tissues-abdomen
Notes: abdomen

## Slide 16: Normal Soft Tissues-flank
Notes: Left flank

## Slide 17: Normal Soft Tissues-arm
Notes: Upper arm

## Slide 19: Where is this mass?

## Slide 20
Notes: Retropectoral implants

## Slide 21: Characterize Mass
After determination of location
Assess
  Shape and margins (image the edges)
  Echogenicity
  Internal characteristics
  Through transmission
  Vascularity
  Dynamic: mobility and compression

## Slide 22: Vascularity
Important to differentiate solid vs cystic
If present, confirms mass is solid
If absent, mass can be solid or cystic
Must show spectral doppler waveform to prove vascularity

## Slide 23: Colour Doppler
Depicts presence and direction of blood flow
Pro:
  Overall view of flow in the region
  Rapid assessment of flow direction and velocity
Cons:
  Limited flow information (esp deep tissue)
  Poorer temporal resolution at increased depth

## Slide 24: Colour Doppler Artifacts
High colour gain: produces colour noise and obscures the true Doppler signal
  Eliminate by setting gain just below the introduction of random colour or speckle
Flash artifact: sudden marked movement of the transducer or the tissue within the field of view
  Eliminate by holding transducer still and asking patient to be still ie breath hold
Mirror image artifact: blood vessel is located very close to a large, highly reflective surface such as the lung
  Eliminate by changing transducer position or window

## Slide 25: Colour Doppler Artifacts
Poor spatial resolution: especially deeper structures
Angle of insonation: vessels-heel toe
Aliasing: abnormally high velocities exceed the rate at which the system can record the velocity correctly
  Methods to eliminate: Increase the PRF or velocity scale; Shift the baseline; Increase the angle of approach; Decrease transducer frequency

## Slide 26: Colour Doppler Controls
Box size

## Slide 27: Colour Doppler Controls
Colour gain: amplifies or decreases the doppler shift signal

## Slide 28: Colour Doppler Controls
Colour scale or Pulse Repetition Frequency (PRF): increases or decreases the maximum velocity that can be displayed without aliasing
The PRF can be altered by the operator to prevent aliasing or to detect low blood flow
As a general rule the PRF should be ideally set at approximately half of the expected velocity of the blood flow in the ROI
The PRF is determined by various controls such as colour box size and velocity range

## Slide 29: Colour Doppler Controls

## Slide 30: Colour Doppler Controls

## Slide 31: Colour Doppler Controls
Persistence or frame averaging
Steering angle

## Slide 32: Colour Doppler Tips
To Increase sensitivity
  Decrease velocity scale or PRF
  Move focal position to the region of interest
  Decrease colour box
  Increase colour gain
To Decrease flash artifact
  Decrease colour gain
  Decrease the depth of field of view
  Decrease sector size
  Use Zoom function

## Slide 33: Power Doppler Imaging
Increased sensitivity to low velocity flow
No direction of flow information
No velocity information
Use on all masses if cannot obtain flow on colour doppler
Decrease 2D gain to increase sensitivity
Sometimes flow can be eliminated with too much transducer probe pressure

## Slide 34: Spectral Doppler
If detect flow on either colour/power doppler, must perform spectral trace to confirm vascularity is present: confirms mass is SOLID
Number one error: incorrect colour and velocity scales
  all techs must learn how to adjust scale on the US machines

## Slide 37: Cystic Mass?

## Slide 38: Solid Mass

## Slide 39: Complex cyst

## Slide 40: Post-traumatic Pseudoaneurysm

## Slide 41: Post-traumatic Pseudoaneurysm
Notes: Scale to low

## Slide 42: Seborrheic keratosis

## Slide 43: Cutaneous mets from lung CA

## Slide 44: Epidermal inclusion cyst/Sebaceous

## Slide 45: Epidermal inclusion cyst/Sebaceous

## Slide 46: Epidermal inclusion cyst/Sebaceous

## Slide 47: Ganglion cyst

## Slide 48: Extensor Digitorum Tenosynovitis

## Slide 49: Baker’s cyst

## Slide 50: MRI Baker’s cyst

## Slide 51: Foreign body

## Slide 52: Foreign Body with inflammation

## Slide 53: Cellulitis

## Slide 54: Phlegmon

## Slide 55: Abscess

## Slide 56: Abscess

## Slide 57: Subcutaneous Hematoma

## Slide 58: Fat Necrosis
Notes: Hyperechoic sucutaneous fat and multiple tiny cysts

## Slide 59: Lipomas
Most common soft tissue tumor
Location: subcutaneous most common
Echogenicity: Hyperechoic, Isoechoic, Hypoechoic
Characteristics: smooth borders, wider than tall, wavy internal echogenic lines (otherwise homogeneous), no acoustic shadowing, minimal to no colour doppler,

## Slide 60: Subcutaneous Lipoma

## Slide 61: Subcutaneous Lipoma

## Slide 62: Subcutaneous Lipoma
Notes: Lipoma peripheral to superficial lobe of parotid gland

## Slide 63: Deep Lipomas

## Slide 64: Not a Lipoma

## Slide 65: Intramuscular hematomas
If making a diagnosis requires significant trauma +/- anticoagulation
Many sarcoma patients report noticing a mass after trauma
At least follow to exclude a mass, if in doubt biopsy or MRI

## Slide 66: Intramuscular hematoma

## Slide 67: Intramuscular hematoma

## Slide 68: Where is this mass?

## Slide 69: Osseous lesion
Normal adjacent anatomy
mass

## Slide 70: Frontal bone osteoma

## Slide 71: Lesion on head of 11 year old?

## Slide 72: What is the next step?

## Slide 73: What is it involving?

## Slide 74: Langerhans Cell Histiocytosis

## Slide 75: Where is this?

## Slide 77: Is there flow within?

## Slide 78: Is there flow within?

## Slide 79: Flow in periphery only

## Slide 80: Perianal fistula with abscess

## Slide 81: Worrisome Features
Any mass > 5cm or Deep location (deep to fascia)
Painful or enlarging mass
Solid heterogeneous lesion
Tissue distortion
Disorganized flow
Lipomatous mass with internal heterogeneity

## Slide 82: Pitfalls
Mass so large, not appreciated
  look for edge of mass, start at normal tissue than scan in toward mass
Field of view too small
  Start with larger field of view to show layers of soft tissue, show borders
Colour doppler
  Make sure small box, drop colour scale/PRF down, velocity scale low, turn up colour gain, use power doppler, prove vascularity with spectral trace

## Slide 84: Inguinal hernias

## Slide 85: Anterior abdominal wall X-section

## Slide 92: Inferior epigastric artery

## Slide 93: Scanning protocol
High frequency linear transducer (10MHz)
Perform at rest and with Valsalva manoeuvers
Scan affected side in both transverse and longitudinal planes (compare with contralateral side if required)
In a standing position, if supine negative
Diagnosis: protrusion of a mass of fat +/- bowel through an abnormal fascial defect

## Slide 94: Right inguinal region
external oblique aponeurosis (E), reflected internal oblique aponeurosis (I), and transversus abdominis muscle (T). Conjoint tendon (C) is medial to deep ring through which passes vas deferens and accompanying artery and vein to form spermatic cord (S). Note superficial ring (straight arrow), inguinal ligament (curved arrow), and transversalis fascia and extraperitoneal fat (F). Read More: http://www.ajronline.org/doi/full/10.2214/AJR.05.1813

## Slide 95: From within abdomen
Inferior epigastric artery (solid straight arrow), rectus abdominis muscle (R), and inguinal ligament (curved arrow) define boundaries of Hesselbach's triangle (H), location of direct hernia. Indirect inguinal hernia passes through deep ring (open arrow), which is lateral to inferior epigastric artery and above inguinal ligament. Location of femoral hernia (asterisk) is usually lateral to lacunar ligament (L) and inferior in relation to medial inguinal ligament. Note conjoint tendon (C) and vas deferens (arrowhead). Read More: http://www.ajronline.org/doi/full/10.2214/AJR.05.1813
Notes: H is hassalback’s triangle for direct hernia
Arrow deep inguinal ring for indirect

## Slide 96: Transducer probe positions
transducer position to evaluate for Spigelian hernia (1), indirect inguinal hernia (2), direct inguinal hernia (3), and femoral hernia (4). Note locations of inguinal ligament (curved arrow), rectus abdominis muscle (R), lateral boundary of Hesselbach's triangle (H) defined by inferior epigastric artery (open arrow), and spermatic cord (arrowhead). Read More: http://www.ajronline.org/doi/full/10.2214/AJR.05.1813

## Slide 97: Number 1
Transverse scan on rectus abdominal muscle, below the umbilicus
Looking for inferior epigastric vessels, just deep to it
Also location for Spigelian hernias

## Slide 98: Rectus Abdominis with IEV

## Slide 99: Spigelian Hernia

## Slide 100: Right Spigelian Hernia

## Slide 101: Move towards Position 2

## Slide 102: Number 2
Follow inferior epigastric vessels from position 1 from rectus muscle toward inguinal canal
Keep IEV in center of image
As the probe is moved inferiorly, the IEV pass from medial to lateral and superficial to deep towards their origin at the external iliac vessels
Once, reached inguinal canal, probe is on deep ring of canal
Site of INDIRECT hernias: fascial defect is lateral to IEV
Small hernia neck

## Slide 103: Transducer Probe 2 position
E is inferior epigastric vessels
A femoral art
V femoral vein
C spermatic cord
Arrow, superior pubic ramus
Notes: E is inferior epigastric vessels
A femoral art
V femoral vein
C spermatic cord
Arrow, superior pubic rami's

## Slide 104: Inguinal ligament

## Slide 105: Deep inguinal ring

## Slide 106: Indirect hernia

## Slide 107: Move towards position 3

## Slide 108: Number 3
Move transducer slightly inferior and medial, but stay above the pubic tubercle
Site of DIRECT hernias: fascial defect is medial to IEV
Large hernia neck

## Slide 109: Direct hernia

## Slide 110: Move towards position 4

## Slide 111: Number 4
Move below inguinal ligament
Femoral artery and vein are in a transverse plane
Saphenous-femoral junction: landmark for inferior aspect of femoral canal (no hernia below this)
Move probe above saphenous-femoral junction
Hernia seen coming from above but medial to femoral vein

## Slide 112: Greater saphenous vein

## Slide 113: Greater saphenous vein landmark

## Slide 114: Femoral Hernia
Notes: At rest and with Valsalva

## Slide 115: Femoral Hernia

## Slide 116: Schematic review
Black oval deep inguinal ring
B DIRECT-hernia is medial to IEV
C INDIRECT- hernia is lateral to IEV
Notes: Black oval deep inguinal ring
B DIRECT-hernia is medial to IEV
C INDirect, hernia is lateral to IEV

## Slide 117: Review
Inguinal hernias : protrude above inguinal ligament
Femoral hernia protrude below inguinal ligament
Indirect inguinal hernia : Neck protrudes lateral to IEA
Direct inguinal hernia : Neck protrudes medial to IEA
Femoral hernia : Neck exit medial to the femoral vein

## Slide 123: Hernias
Size of fascial defect
Size of hernia sac
Contents of sac:
  Fat
  Bowel
  other

## Slide 124: Hernias
Reducible with transducer probe pressure
Irreducible with transducer probe pressure
Obstructed/incarcerated : very narrow neck and bowel loop is trapped
Strangulated: compromise of the blood supply
  Bowel peristalsis, bowel wall thickening, fluid in bowel loop, fluid in sac, hyperechoic fat, thickening of hernia sac, doppler flow of contents

## Slide 126: Incarcerated abdominal hernia

## Slide 127: Incarcerated abdominal wall hernia with dilated nonreducible small bowel loops and fluid in the hernia

## Slide 128: Strangulated inguinal hernia with dilated bowel loop

## Slide 129: Don’t forget
Repeat standing
Look for masses, lymphadenopathy, fluid collection, abscess or aneurysm

## Slide 130: Diastasis Recti

## Slide 131: Linea alba

## Slide 132: Progressive weakening of Linea Alba

## Slide 133: Static & Dynamic Image of Diastasis
Measure distance in between
Valsalva and remeasure

## Slide 134: Diastasis

## Slide 135: Diastasis

## Slide 136: Diastasis

## Slide 138: Bibliography
P. Yoong et al. The inguinal and femoral canals: a practical step-by-step approach to accurate sonographic assessment, Education exhibit poster, ECR 2014 / C-1243 .
Tomasso Vincenzo Bartolotta , Abdominal and Inguinal hernias, University of Palermo, June 19, 2014 Video